## Slide 1: Probabilistic Analysis of Structure
Group member
Delos-Haoran Liang
Atom-Yatong Wu
Rick-Shoupei Wang
Group 3

## Slide 2: Contents
Background
Structural analysis(by Atom-Yatong Wu)
  Structure layout
  Loads
  Displacement method
Probabilistic analysis(by Delos-Haoran Liang)
  Uncertainties in capacities
  Uncertainties in loads
  Fragility analysis
Additional insight(by Rick-Shoupei Wang)
  Expected losses
  Measures to reduce the losses
Conclusion

## Slide 3
In foreign countries, the idea of container house has been widely used.
A container can be transformed into a warm house with windows and doors after a little change.
Background

## Slide 4
Domestically, such containers are commonly used as dormitories for workers on construction sites.
It is worth studying whether such buildings are safe in daily life and stable in windy weather. Therefore, we chose the most common container on the construction site as the research object for structural analysis and research.
inexpensive
sturdy and durable
construct easily
Background

## Slide 5: Contents
Background
Structural analysis(by Atom-Yatong Wu)
  Structure layout
  Loads
  Displacement method
Probabilistic analysis(by Delos-Haoran Liang)
  Uncertainties in capacities
  Uncertainties in loads
  Fragility analysis
Additional insight(by Rick-Shoupei Wang)
  Expected losses
  Measures to reduce the losses
Conclusion

## Slide 6
We assumed the element DF is loaded by a uniform load q and the length is L; A B C E node is the rigid joint; node D F is the hinge joint individually;
The structure have 3 superfluous constraint.
Structure layout & Load
Fig.1. Schematic
Fig. 2. Vertical uniform load

## Slide 7
We can assume the angle is 1
1. Fix the structure and then break it down
=
+
2. Analyze the node E
We can look up in the table:
Displacement method

## Slide 8
We can look up in the table:
4. Build the equation of displacement method
Displacement method
3. Analyze the node E

## Slide 9
5. We can get:
6. Calculating the bending moment of the left side of node E

## Slide 10
7. Draw the final internal force diagrams
(a) Bending moment diagram
(b) Shear force diagram
Fig. 3. Internal force diagrams

## Slide 11
8. Draw the internal force diagrams when the structure is affected by a left wind
(a) Bending moment diagram
(b) Shear force diagram
the structural analysis:
Fig. 4. Left wind load
Fig. 5. Internal force diagrams

## Slide 12: Contents
Background
Structural analysis(by Atom-Yatong Wu)
  Structure layout
  Loads
  Displacement method
Probabilistic analysis(by Delos-Haoran Liang)
  Uncertainties in capacities
  Uncertainties in loads
  Fragility analysis
Additional insight(by Rick-Shoupei Wang)
  Expected losses
  Measures to reduce the losses
Conclusion

## Slide 13: Uncertainties in capacities
Description
We select hot rolled ordinary I-beam of Q235 steel, this kind of I-beam is used for a column with a hinged upper end and a fixed one at the lower end, and the length of the column is 8m.
Fig. 6. I-beam
Size(mm) |  |  |  |  | cs-area (cm2) | x-x axis | 
h | b | d | t | R |  | WX (cm3) | IX/SX (cm)
200 | 100 | 7.0 | 11.4 | 9.0 | 35.5 | 237 | 17.2
Table 1: Standard of I-beam
Steel |  | Bending stiffness f (N/mm2) | Shear stiffness fv (N/mm2)
Type | Diameter(mm) |  | 
Q235 steel |  | 215 | 125
Steel |  | Bending stiffness f (N/mm2) | Shear stiffness fv (N/mm2)
Type | Diameter(mm) |  | 
Q235 steel |  | 215 | 125
Table 2: Strength design value

## Slide 14
Description
1. According to our preliminary calculation, the maximum shear force loading on the structure is far smaller than the design
value of shear force, so we only took the bending failure into consideration.
2. We didn’t consider the destruction of the boards, and we assumed the loading on boards will transmit to the columns on
both sides uniformly.
3. The formula for calculating standard value of maximum bending moment is as follows(Chen & Gu, 2014):
Me obeys Gamma Distribution(Smith, 2011), the related parameters are shown in Table 3.
random variable | mean | coefficient of variation(Liu, etc., 2020)
Me(kN · m) | 53.503 | 0.016
Table 3: Parameters of Gamma Distribution

## Slide 15
MC algorithm through MATLAB
Notation
NMC number of Monte Carlo simulations
Fig. 8. Histogram of frequency when NMC = 10,000
Fig. 7. MATLAB code for MC algorithm

## Slide 16: Uncertainties in loads
Description
According to Load Code for Building Structures (GB50009-2012) in China, the statistical samples of snow pressure and wind velocity obey the Extreme Value TypeⅠDistribution.
The distribution function of the snow pressure and wind velocity is as follows(GB50009-2012):

## Slide 17
Description
1. To simplify our analysis, we ignore the loads caused by snow pressure and the dead weight of the structure, we will
only focus on the wind loads.
2. According to GB50009-2012, the wind loads are calculated by basic wind pressure 0 which obeys a relationship
with basic wind velocity v0:
GB50009-2012 only provides the data of basic wind pressure, so we assumed that basic wind pressure also obeys
Extreme Value TypeⅠDistribution, the related parameters are shown in Table 4.
random variable | mean(Peking, GB50009-2012) | coefficient of variation
(kN / m2) | 0.5 | 0.01
random variable | mean(Peking, GB50009-2012) | coefficient of variation
 | 0.5 | 0.01
Table 4: Parameters of Extreme Value TypeⅠDistribution

## Slide 18
Wind Load
The formula for calculating wind load is as follows(GB50009-2012):
Given windward width of the structure B = 8m, we obtain the specific values of the structure according to GB50009-2012,
and we will put the detailed calculative process in our final written report, the values are shown in Table 5.
coefficient |  |  | 
value | 2.04 |  | 0.65
coefficient |  |  | 
value | 2.04 |  | 0.65
Table 5: Values of coefficient
Fig. 9. Equivalent uniform load on our structure

## Slide 19
Wind Load
Fig. 11. Histogram of frequency when NMC = 10,000
Fig. 10. MATLAB code for MC algorithm

## Slide 20: Fragility analysis
Label | Threshold level (mm)
T1 | 0.012%B = 0.96
T2 | 0.016%B = 1.3
T3 | 0.02%B = 1.6
T4 | 0.024%B = 1.9
T5 | 0.028%B = 2.2
In Fig. 12 the dimensional displacement thresholds used in
this study(T1 to T5) were defined as a function of the building
width, variable between 0.012%B and 0.028%B(B = 8 m).
These thresholds, listed in Table 6, were selected as a first
attempt at defining appropriate and realistic limit states(e.g.,
Maximum lateral drift criterion)(Smith, 2011).
Table 6
Thresholds for use in the fragility analysis of our structure.
Fig. 12. Example of structural fragility curves for uncertain
distribution of Me as a function of the increased velocity.

## Slide 21
Probability of failure
Fig. 14. Bending moment diagram (unit q kN · m)
point of bending failure
Fig. 13. Flow chart of the calculation of the P(Failure)
Application of unit load method:

## Slide 22
Probability of failure
Fig. 15. Probability of failure of our structure at B = 12m,
computed by MC method --（a）scatter plot of 100
consecutive MC simulations as a function of the No. of
Monte Carlo simulations(NMC)， = 0.0111 when NMC =
100,000;（b）Coefficient of Variation vs. NMC.
a
b
Table 7
MC validation: run time vs. NMC.
NMC | Average relative run time a
1,000 | 0.0097
5,000 | 0.0483
10,000 | 0.0965
50,000 | 0.4961
100,000 | 1.0000
a Run time relative to NMC = 100,000.

## Slide 23
Suggestion for design value
Fig. 16. Probability of failure as a function of the increased width
of the container when NMC = 10,000.
Without additional support, the unit lode q is
proportional to the width B, so with the increase of B, the probability of failure rises respectively.
If the maximum tolerance of the P(Failure) = 0.01%,
then the theoretical threshold of the design value of the width will be 11.6m.
However, in fact, the realistic design value of the width of the type of our container is usually between
8m and 10m, due to the unpredictable uncertainties caused by manual manipulation especially when installing, so setting up the design value a bit less than the theoretical threshold can guarantee the safety to the utmost extent.

## Slide 24: Contents
Background
Structural analysis(by Atom-Yatong Wu)
  Structure layout
  Loads
  Displacement method
Probabilistic analysis(by Delos-Haoran Liang)
  Uncertainties in capacities
  Uncertainties in loads
  Fragility analysis
Additional insight(by Rick-Shoupei Wang)
  Expected losses
  Measures to reduce the losses
Conclusion

## Slide 25: Additional insight
Expected loss
Expected loss: the loss of construction refers to the loss of value caused by the diminishing utility of buildings due to various reasons during the using of buildings (Shen, 2001).
Material loss
Invisible waste
Energy loss, material loss (concrete, steel), structure damage
Economic loss, space waste
Building loss is an important problem in building construction. And reasonable estimation of loss can effectively prolong the lifespan of buildings and save energy to achieve sustainability(Zeng, 2012).

## Slide 26: Expected loss in the structure
Material factors: Dimensional error of steel, corrosion of steel
Fig. 17. Corrosion of steel
Economic factors: Changes in material prices, reduced utilization of space
Determination of building loss (Gao, Zhang, 2021):

## Slide 27: Measures to reduce the losses
Protection of Steel——Anti-rust paint
TN-922G (Specially developed for long-term exposed steel) (Ye,2012)
The material is made of inorganic cementitious materials and non-toxic polymer additives.
Properties:
Non-toxic
Tasteless
Non combustible
Nonvolatile
Corrosion resistance
Strong sealing
Simple operation
No special maintenance needed
Preparation of equipment
Spray sand and clean rust
Surface treatment with wire brush
Blending coating
Brushing
Fig. 18. Workflow

## Slide 28: Measures to reduce the losses
Refined management to reduce the loss of steel (Bi, Ye, 2014)
Build backstage steel management system.
Build using scattered material management system.
Build accountability system.
Economic measures

## Slide 29: Contents
Background
Structural analysis(by Atom-Yatong Wu)
  Structure layout
  Loads
  Displacement method
Probabilistic analysis(by Delos-Haoran Liang)
  Uncertainties in capacities
  Uncertainties in loads
  Fragility analysis
Additional insight(by Rick-Shoupei Wang)
  Expected losses
  Measures to reduce the losses
Conclusion

## Slide 30: Conclusion
Related areas
  Structural analysis: Structural mechanics, Material mechanics
  Probabilistic analysis: Probability Theory, Numerical analysis
  Additional insight: Material Science, Engineering Management
Strengths
  Visualization: To the best of our knowledge, we utilize MATLAB and Origin to perform our results, which are
  generally thought to be precise and intuitive.
  Simpleness & Effectiveness: We build a simple and effective methodology without considering all the details
  of the structural and probabilistic analysis.
Weakness
  Missing the consideration of the combination of the influences by all possible loads.

## Slide 31: Reference list
Chen Shaofan, Gu Qiang. Steel structure foundation[M].Peking: China Architecture & Building Press, 2014.48-51.
Liu Jiaxing, Li Yeping, and Xie Xianjiao. Evaluation of Uncertainties in Tensile Strength Measurement of Q235 Steel. Physical and Chemical Inspection-Physical Volume 56.6(2020):27-28.
Ministry of Construction, PRC. “GB50009-2012, Load Code for Building Structures.”(2012).
Smith, Marra A. , and Luca Caracoglia. “A Monte Carlo based method for the dynamic “fragility analysis” of tall buildings under
turbulent wind loading.” Engineering Structure 33.2(2011): 410-420.
Shen Liangfeng. Using Fuzzy Theory Determine the Proportion of Building Damage. J.OF Wuhan Urban Construction On Institute Vol.18 No.2 Jun.2002
Zeng Miaoxin. Optimize Building Construction Techniques to Reduce Building Energy Loss. Private Science and Technology. 43.8(2012):313
Gao Xiaolou, Zhang Ting. Construction Materials Management Method Based on BIM. Engineering management. 12(2012):105-106
Ye Jinfeng. Study on Anticorrosion Technology of Long-term Exposed Rebar. China Three Gorges Construction. 06(2016):20-21

## Slide 32
Thanks for Listening